## Slide 1: “Placenta-on-a-chip” – replicating organ functions in a microfluidic chip
Jeremy Caplin

## Slide 2: Issues with current drug testing methods
In vivo:
  unethical
  Can Often be an inaccurate representation of actual human responses
  expensive
In vitro
  Difficult to replicate the complexity of the human anatomy
  Typically miss some sort of important physiological trait in favor of simplicity (two-dimensional models, static conditions, etc.)

## Slide 3: Organ-on-a-chip
The intersection of in vivo and in vitro drug testing
Centered around recreating the in vivo microenvironment
Has the potential to replicate human organs, and connect them to create a “body-on-a-chip”

## Slide 4: Organ-on-a-chip
Take advantage of microfluidic phenomena
Minimal products and materials
Relatively Easy to manufacture
Physiologically similar to the body
Replace unethical alternatives

## Slide 5: Chip layout
Width: 400 microns
Height: 100 microns
Midsection length: 1 Cm
Inlet/outlet diameter: 1 mm
Membrane thickness: ~10 microns
Inlet/outlet to midsection angle: 135°

## Slide 6: Chip design
Fabrication Techniques
  Polymethyl methacrylate (PMMA)
    micromilling
  Polydimethylsiloxane (PDMS)
    Soft lithography -> Master mold
  Collagen vitrification

## Slide 7: Liver-on-a-chip
System consists of a syringe Pump delivering media into the chip at a constant flow rate, with outlet streams collected as waste
Can sustain multiple trials at once, allowing many different parameters to be tested (concentration of ethanol, duration of cell seeding before exposure, etc.)

## Slide 8: Liver-on-a-chip
Top layer
  Cells
    Human umbilical vein endothelial cells (HUVEC)
  Media
    EGM-2
Bottom layer
  Cells
    Hepatoma cells (Hepg2)
  Media
    DMEM with supplements

## Slide 9: Placenta-on-a-chip
Top layer
  Cells
    Human umbilical vein endothelial cells (HUVEC)
  Media
    EGM-2
Bottom layer
  Cells
    Syncytiotrophoblast cells (BEWO)
  Media
    F-12k

## Slide 10: Future work
Future Work
  100% animal free design
    Focus: extracellular matrix and serum
  Marker identification
    E-cadherin
  Viability tests in ethanol
    Mapping non-ideal environments
  TEER measurements

## Slide 11: Thanks for listening!
I’d like to thank the lush foundation for this award, as well as recognize the efforts of Dr. Nastaran Hashemi and the hashemi lab at iowa state university, and Dr. Noo Li Jeon and the MBEL lab at seoul national university
FUNDING PROVIDED BY IOWA STATE UNIVERSITY, WITH ADDITIONAL FUDING PROVIDED BY THE NATIONAL SCIENCE FOUDATION AND PETA