## Slide 1: Lush Prize 2015
“Body-on-a-Chip; In vitro Human Models for Drug and Chemical Testing”

## Slide 2: The Team
Michael L. Shuler – Cornell University
mls50@cornell.edu
James Hickman – University of Central Florida
jhickman@ucf.edu
Mandy B. Esch - Cornell University, Syracuse University
mbesch@syr.edu
Tracy Stokol – Cornell University
ts23@cornell.edu
Gretchen Mahler – Cornell University, State University New York at Binghamton
gmahler@binghamton.edu
Hickman & Shuler have started Hesperos, Inc.

## Slide 5: Basic Concepts
Animal models are not very effective in drug development
  Ethical, cost, time issues.
  Poor predictors of human response: 11% of drugs entering clinical trials came out as approved products.
      For every 50 drugs found safe for animals only 1 proves safe in humans (2%); one drug company finds 6% of animal trials predict human response
  In vitro models using human cells/tissues provide potential models with improved accuracy.

## Slide 6: Search for Replacements
Both regulatory agencies, pharmaceutical and chemical companies recognize problems with animal studies
The current drug development process is too costly; both regulators and companies open to new technologies that are more accurate and cost-effective
Increased success in clinical trials from 11% to 33% would have big economic impact; replacements need not be perfect, only better than animals

## Slide 7: Developing a Human Surrogate “Human-on-a-Chip”
Goal: Integration of organs-on-a-chip to form a “body-on-a-chip”
Why: Predict in pre-clinical studies how humans will respond to drugs or chemicals
How: Experimental device guided by Physiologically Based Pharmacokinetic (PBPK) model; more than a simple multi-organ system: it attempts to maintain physiological relationships among organs and add biological function beyond metabolism
When: Conceived Spring 1989 (US Pat. 5,612,188); microfabricated systems in 1998 (US Pat. 7,228,045)

## Slide 8: Mathematical Models Can Predict Drug Distribution
PBPK (Physiologically-Based Pharmacokinetic) computer models treats human body as a series of interconnected compartments
Compartments are reactors, absorbers, or holding tanks
PD (Pharmacodynamic model) predicts pharmacological effect
Lung
Liver
Blood
PBPK model

## Slide 9
Organ volume ratios translate into ratios of microfluidic chamber volumes.
Fluid residence time per organ translates into fluid residence time per organ chamber.
A passive fluid flow split achieves the required fluid flow rates.
The chip is operated with a common medium in which all tissues will grow.
Physiologically Designed Systems
Human body
PBPK
Body-on-a-Chip
Lung
Adip.
Bone
Heart
Kidney
Muscle
Skin
Liver
Gut
Spleen
Arterial Blood
Venous Blood
Brain
Gut
Kidney
Adip.
Liver
Bone
Plasma
well perfused
poorly perfused
Chip PBPK

## Slide 10: Design Criteria to Emulate PBPK
Realistic ratio of cell mass in one organ to another
Mimic flow split of blood during recirculation
Residence time in “organ/tissue” compartment is realistic
Physiological shear rates
Where possible ratio of liquid to cells in a compartment is physiologic
Biological response of cells in compartment is authentic: tissue engineered constructs may be ideal

## Slide 11
 | Tumor | Liver | Marrow
Calculation |  |  | 
Residence time (s) | 70 | 52 | 128
Velocity (um/s) | 71.5 | 160.7 | 53.6
Measurement |  |  | 
Residence time (s) | 69.7±3.8 | 49.7±3.5 | 136.5±2.9
Velocity (um/s) | 68.9±1.6 | 167.9±6 | 58.6±0.5
Liver(HepG2/C3A)
Tumor (HCT-116)
Marrow (Kasumi-1)
Fabricated from silicon
Based on previous μCCA
Designed to test drugs for colon cancer
Liver/tumor/marrow
Flow residence times are matched to physiological values
Design and Assembly: Passive Flow Control
Polycarbonate
Silicon
Aluminum
No Valves Required!

## Slide 12: System Operation
Medium is recirculated (200μL) to mimic the body’s recirculation 6~8 chips, operating time: 3 days without medium exchange
Medium reservoir
μCCA
Bubble trap

## Slide 13: Example: Naphthalene
Toxicology In Vitro 9:307 (1995); Biotechnol Prog. 16:33, 471 (2000); Biotechnol. Prog. 20:316, 338, 590 (2004)
Naphthalene (3 organ chambers)
  Demonstrate capability to define or confirm mechanism of action and explain why mice and rats differ in terms of toxicological response
  Demonstrate that naphthalene toxicity is due to formation of naphthoquinone in the liver and circulation to the lung

## Slide 14: Example: Multidrug Resistant Cancer
MDR (4 organ chambers- liver, bone marrow, uterus(both MDR & sensitive), other tissues)
  Test combination treatment (Doxorubicin, cyclosporine & nicardipine)
  Found that MDR suppressors have synergistic interaction
  Can use device and PBPK to estimate appropriate drug doses for in vivo trials
Tatosian, DA and ML Shuler. 2009. Biotechnol. Bioeng. 103: 187.

## Slide 15: Example: Colon Cancer with Prodrug
Treatment with Tegafur (prodrug for 5 Fluorouracil) and Uracil (inhibits degradation of 5FU) for colon cancer
Liver (metabolism) – colon (target) – marrow (Kasumi-1) all entrapped in hydrogels/3D culture
Response consistent with clinical observations:
  Liver cells required for toxicity to colon cancer
  Uracil enhances toxicity
  Semi-quantitative
Sung, JH and ML Shuler. 2009. Lab on a Chip 9” 1385.

## Slide 16: Design to Simplify Operation
Jong Hwan Sung, Carrie Kam, Michael L. Shuler, A microfluidic device for a pharmacokinetic-pharmacodynamic (PK-PD) model on a chip Lab on a chip, 2010, (10: 446, 2010)

## Slide 17: Multichamber device on rocker platform made from silicon sheets and polycarbonate frame; low cost; easy to modify Easy to implement (rapid set-up and minimal operator training) Low cost format (no pump, multiple units on a rocker platform, optical and electrical access) Robust operation (no gas bubbles, removes tubing that causes dead volumes and unphysiologic absorption, no moving parts to fail)
Cornell “Pumpless” System
Easy set up, low cost, robust

## Slide 18: Can Barrier Models be Incorporated into Body-on-a-Chip Systems?
Examples of important barrier tissues:
  Gastrointestinal (GI) Track
  Lung Epithelium
  Skin
  Blood Brain Barrier
Barriers control entry of drugs into systemic circulation or into specific tissues (e.g. brain)
To mimic oral uptake, inhalation, or adsorption, need barrier/systemic circulation model

## Slide 19: Building Models of Each “Organ” Compartment Using Human Primary on iPS Cells
GI tract
Skin (with Christiano/Columbia)
Vasculature
Liver (with Applegate/RegeneMed)
Blood brain barrier (from Shusta/U,WI)
Cardiac (Hickman at UCF)
Neuromuscular junctions (Hickman at UCF)
Other tissues still based on cell lines but will be replaced with human primary or stem cells as project develops

## Slide 20
All epidermal layers formed
Skin barrier function maintained
Basal keratinocytes remained proliferative
The HSEs were prepared and successfully transported from Columbia to Cornell University in transwell plates
HSEs were punched out in 3 mm circles and transferred into HSE-on-chip platform
Skin constructs were maintained for 3 weeks on-chip
Human skin equivalents (HSE)-on-a-Chip
Long-term maintenance of HSE-on-chip
Drug testing using HSE-on-chip
Doxorubucin treatment causes a spatial detachment of the basal layer along the epidermis-dermis interface
One week of doxorubucin treatment inhibited keratinocyte proliferation
Jointly with Christiano Lab, Columbia
Lab Chip (15):882-888 (2015)

## Slide 21
Human Blood Brain Barrier-on-a-Chip (BBBoC)
In vitro BBB model from human iPS cells (from E. Shusta & S. Palecek)
The BBB constructs were prepared from iPSC derived brain microvascular endothelial cells (BMEC) co-cultured with astrocytes on a porous membrane;
BMEC
Astrocytes
Rocker platform
Reservoirs
BBB construct
microchannels
Bottom electrodes
Top electrodes
R
Trans-Endothelial Electrical Resistance (TEER) sustained at high levels
Tight Junctions formed
Human Blood Brain Barrier-on-a-Chip (BBBoC)
BBB construct barrier functions sustained on chip

## Slide 22: Broadening Potential Impact
Measure function (mechanical and electrical as well as metabolic/chemical)
Requires different types of organ modules
Serum-free, common medium needed
Can support 7 different organ modules in serum-free medium; removes dependence on animal serum
Example: Stancescu, et al, Biomaterials 60; 20, 2015 (Hickman Lab)

## Slide 23
Polycarbonate lid
with reservoirs**
PDMS vasculature
Polycarbonate
membrane
Silicone gasket
Polycarbonate
bottom plate
Cantilever and cMEA chips
Polycarbonate
frame
with PCB**
HSL Integrated CardioVascular Module
Lid and PCB not shown
(for clarity)
**

## Slide 24: Electrophysiology – hIPSC cardiomyocytes on MCS MEA Conduction velocity measurement
stimulated
Calculated Conduction velocity = 0.42 m/s
QT interval

## Slide 25
Bi(o)morph Force/Displacement Detection Schemes
I. Deflection (optical lever)
II. Piezoresistive (embedded strain gauge)
Laser
photodetector
v

## Slide 26
Functional Evaluation- hIPSC cardiomyocytes on HSL Integrated Cardiac Module
MEA Recording
Cantilever Recording
Electrical
Force

## Slide 27: Testing with cardioactive compounds
Compound | Mode of Action | Effect
Norepinephrine | Adrenergic agonist | n = 3, Increase beat frequency and contractile force
Epinephrine | Adrenergic agonist | n = 4, Increase beat frequency and contractile force
Acetylcholine | Parasympathetic neurotransmitter; cardioprotective | n = 4, effect inconclusive; confirm AchR expression with immunostaining
Verapamil | L-type calcium channel blocker; antiarrhythmic | n = 3, decrease beat frequency and contractile force Decrease conduction velocity; Prolongs QT interval
Sparfloxacin | Non-cardiac drug; antimicrobial | n = 1, QT prolongation as a side effect
Sotalol | Anti-arrhythmic | n = 2, Decrease conduction velocity; Prolongs QT
Propanolol / Metoprolol (after Epinephrine) | Anti-arrhythmic, beta-blocker | n = 2, Counteracts adrenergic effects

## Slide 28: Basis for Advanced Multi-Organ Systems
Chemical, biological, electrical & mechanical responses
Both in situ (online) measurements and off-line from “blood” surrogate
Can capture impact of metabolic conversions and organ-to-organ exchange
PPBPK model of device leads to PBPK of human response to predict human response to a variety of exposure scenarios

## Slide 29: 13 Organ Device

## Slide 30: Toward a Physiological Model
A rocker platform design reduces problems associated with pumps (e.g. gas bubbles)
2 layered system allows direct organ to organ communication: Barrier tissues to internal organs
Organ sizes are scaled proportionately to each other using average adult human male organ volumes (Price 2003)
Channel dimensions calculated to match the flow to obtain physiological organ residence times

## Slide 31: Hesperos,Inc.; Making Systems Widely Available
1. Goal is to commercialize Functional “Body-on-a-Chip” technology as well as individual organ systems for humans.
2. Work with customer to custom design systems as well as offer standard tests for cardiac, NMJ, liver, muscle and combinations thereof; available skin & GI soon.
3. Functional tissues; Chemical, electrical, mechanical, and biological outputs measured.
4. All systems in serum free defined medium utilizing human cells.
5. Shuler as CEO; J. Hickman as Chief Scientist; Jeff Anderson as business manager (janderson@hesperos.net)

## Slide 32
Colleagues | Prior PhD Students | Post-Doc
Ray Glahn | Lisa Sweeney | Mandy Esch
Sung June Kim | Kwan Viravaidya | Jean Matthieu Prot
Don Cropek | Aaron Sin | H. Erbil Abaci
Don Kim | Dan Tatosian | Ying Wang
Jay Hickman | Gretchen McAuliffe | Joyce Chen
Angela Christiano | Hui Xu | 
Dawn Applegate | Jay Sung | 
Brian Davis |  | 
John March | Funding | 
Xiling Shen | Nanobiotechnology Center, NSF, U.S. Army (CERL) NIH | 
Steven Lipkin | CNF (Cornell Nanofabrication Facility), NYSTAR | 
Acknowledgements