## Slide 1: The KeratinoSens™ assay
A test for the AOP of skin sensitization adopted by the OECD

## Slide 2: Contents
Introduction
The molecular mechanism behind KeratinoSens
How the KeratinoSens cell line works
Practical steps
The readout – dose response curves
Validation and benchmarking
Applicability domain
Use of in vitro testing to design and identify safer molecules
Application in AOP based integrated testing strategies

## Slide 3: Introduction
Skin sensitization key toxicological endpoint for topical products (cosmetics / fragrance)
Skin sensitizers react with skin proteins and then trigger an immune reaction
Classically assessed by animal tests Can we switch to test, which is based on a cell line?
Key question: Can cells ‘sense’ reactive molecules – and discriminate them from non-sensitizers?
YES – Pathway for the detection of reactive electrophilic xenobiotics is present in all cells
    Keap1-Nrf2-ARE pathway

## Slide 4: The Nrf2-Keap1-ARE pathway: An electrophile-sensing pathway
A. Natsch, Toxicol. Sci. 2010, 113.

## Slide 5: KeratinoSens™: Mechanism of reporter cell line for Nrf2-pathway
Nrf2
ARE element : Genetic switch
Nrf2-protein: Transcription factor: ‚Presses the button‘ on ARE
Keap1: Sensor protein, activates Nrf2 in presence of reactive molecule
Keap1
SH
SH
SH
Luciferase gene
ARE
DNA
Antioxidant response
element from AKR1C2
SV40
SV40 promotor for stable background
Reaction at sensor surface
Luciferase gene
from firefly
R. Emter, G. Ellis, A. Natsch, Toxicol. Appl. Pharmacol. 2010, 245.
Easily measurable

## Slide 6: KeratinoSens™ assay protocol
Cells grown in 96-well plates for 24 h
Chemicals dissolved in DMSO (solvent)
Chemicals added to cells at 12 different concentrations
Incubation for 48 hours
Determination of cell viability
Determination of luciferase activity
  Lysis of cells
  Addition of luciferin substrate
  Measurement of light output

## Slide 7: KeratinoSens™ read out: Typical dose-response curve
In each test, chemicals are tested at 12 different concentrations
Example for the hair dye component p-phenylendiamine (strong sensitizer)
% viability
fold luciferase induction
Chemical surpasses threshold, positive rating
A. Natsch, R. Emter, Arch Toxicol 2015, 89.

## Slide 8: Validation
For an in vitro assay to become broadly accepted, four key steps are required
Define a detailed and exact protocol = Standard operating procedure (SOP)
Prove the assay is reproducible when performed in the same lab over prolonged time Intralaboratory reproducibility
Prove the assay gives same result when performed in independent labs on the same, blind-coded chemicals Interlaboratory reproducibility
Prove the assay is predictive against historical animal (or better human) data Benchmarking against historical data, assessed by Cooper statistics

## Slide 9: Validation: Intralaboratory reproducibility
Very similar results were obtained for chemicals tested in our lab twice, five years elapsed between the two assays
R. Emter, A. Natsch, Toxicol In Vitro 2015, 29

## Slide 10: Validation – Interlaboratory reproducibility for DNCB
A. Natsch, C. Bauch, L. Foertsch, et al., Toxicol. In Vitro 2011, 25.

## Slide 11: Validation – Predictivity
Accuracy of 85% in predicting a well-curated list of chemicals (Evidence from multiple animal tests and, partly, human data)
Accuracy between 75% and 80% on larger lists with only LLNA evidence
  Accuray = % of correct predictions of n chemicals
R. Emter, G. Ellis, A. Natsch, Toxicol. Appl. Pharmacol. 2010, 245.

## Slide 12: The KeratinoSens™ : Validation with authorities
The European Center of validation of alternatives to animal testing (ECVAM) did evaluate results from 2011 – 2013
First biological assay for skin sensitization receiving ECVAM approval in Feb. 2014
OECD guideline (Adopted Feb 2015)

## Slide 13: Applicability domain
KeratinoSens was mainly tested against low molecular weight chemicals
  Only for these we have solid in vivo data to compare against
  Most known skin sensitizers fall into this class
Limitations
  Cosmetic companies want answers for plant extracts – but also animal tests were never validated for these
  Best option: test single constituents
  Very high cLogP / non-soluble substances
  Some phenolic prohaptens (opportunities for S9 assay)
  Chemicals with exclusive amine-reactivity (can be detected with peptide reactivity assay)
  Larger polymers – preliminary data show limitations for silicones
  Probably overprediction for some flavonoids / polyphenolics from plants

## Slide 14: Use of in vitro testing to design and identify safer molecules
Key benefit of in vitro testing, beyond animal welfare, is ability to test many molecules early in discovery process
We screened 630 molecules in KeratinoSens and peptide reactivity within last 18 months
  Impossible in classical toxicology paradigm!
Structure-activity relationship can be established
This led to new hypoallergenic fragrance leads

## Slide 15: Use of data in an Integrated testing strategy (ITS)
OECD AOP concept proposes to combine assays which address different steps in the adverse outcome pathways
ITS (integrated testing strategy) should then be able to give more robust / more accurate prediction of hazard, and ideally, potency
A number of studies have shown the use of KeratinoSens / Nrf2 induction data in combination with peptide reactivity
More recent studies also showed combination of KeratinoSens with Dentritic cell activation assays (MUST / h-Clat assays)
At Givaudan we always run KeratinoSens in parallel with peptide reactivity test (LC-MS based and kinetic tests)

## Slide 16: The deterministic ‘democracy’ weight-of-evidence approach ITS for hazard ID
Simple approach: take a ‘majority voting’ of the three in vitro assays
  (KeratinoSens, h-CLAT, DPRA)
Proposed by BASF, based on 54 chemicals
Recent analysis on 103 chemicals with human and LLNA data
D. Urbisch, A. Mehling, K. Guth, et al., Regul. Toxicol. Pharmacol. 2015, 71, 337.

## Slide 17: More sophisticated approach for determining sensitizer potency
Use the quantitative readouts form in chemico, in silico and in vitro data
Bayesian net integrates data to predict LLNA potency class
Ongoing discussions at OECD and ECHA – what is best model?
J. Jaworska, Y. Dancik, P. Kern, F. Gerberick, A. Natsch, Journal of Applied Toxicology 2013, 33.
KeratinoSens output
Calculated bioavailabilty
DPRA output
Dendritic cell
activation
Mechanistic
in silico
model
LLNA
target

## Slide 18: Acknowledgements
Ring study partners
Stefan Onken, Hendrik Reuter, Andreas Schepky, Beiersdorf
Leslie Foertsch, Frank Gerberick, P&G
Caroline Bauch, Robert Landsiedel, BASF
Kim Norman, Erin Hill, Rodger Curran, IIVS
Givaudan Bioscience Group

## Slide 19: Thank you
Contact
roger. emter@givaudan.com